 MCU Test – 2x2
  Ron Miller Jan 2018
    instructables.com/member/RonM9

Made especially to test the wiring and operation which has 2 buttons and 2 LEDs

Basic Testing of any MCU, with attached 2-4-ish LEDs + ... (Audio separately optional).
Test Operations exercise Buttons, LED operation and lighting levels, timing, interrupts, EEPROM storage, USB-Serial I/O and optionally buzzer &/or speaker.

During initialization 'setup', LEDs will be steped through (with audio alerts); an analog read of a reference voltage is made, and calculated Vcc is SerialPrinted, as well as the number of 0.1 volts over 3.0 is counted out on the Led display. Then Led1 starts flashing at 1/2 Hz until the first button is pressed.

The main/selection menu is shows L1 Flashing and advanced with btn2 through L2 flashing, L1 Bright, L2 Bright one after the other representing the four available functions. Button1 is still used to make a selection.
Below is an overview of functions with Bold highlighting of differences made to accommodate Two-button operation.
For greater general details refer to the 4x4 user manual MCU_Test_4x4.odt.

    1: btnReporting()	Verifies each button and Led wiring assignment and operation. Can be checked by	noting Led display corresponds to the button(s) being pressed, and/or by Serial printouts.
To enter from menu hold Btn2.

   2: Scales()	For checking standard Light and Audio levels (& thus delay period timing).
A 'waiting' display will be shown, double stepping thru leds @1Hz
First scale: 'dim'/lowTone, 'lit'/beep, 'brt'/Beep and flashing/buzz.
Next operation allow going through 0-10 levels of Led brightness and audio Notes.
B2 to up levels, B1 sound note.
Hold Btn2 to step thru the 3 display&sound operations, exits after 3rd stage.
First simulations is of a Cylon helmet display and sound. Btn2 for next.
??

    3: Timer()	Exercises delay()/millis() period timing.
Optionally (via dual btn press Btn1+4) ISR millisecond timing accuracy.
Once selected, this timer flashes an LED every one second; beeps every 10 secs and advances the flashing led every 30 secs (led 1-2 representing up to 60 seconds).
For stop watch functionality: use Btn1 to stop & restart and Btn2 to pause & subsequently continue.

    4: PerfTest() MicroControlerUnit practical Performance Test. Counts how many times a second a set of Analog & Digital I/Os with Floating Pt. & Integer math plus general logic can be done (“MCU marks”). Also exercises EEPROM storage, and reports the last test results having been stored.
Note that the code is intentionally not optimized, due to bench-marking purposes.
After a fixed period of testing it prints the Performance rating of “ MPU Marks”

Exiting tests, in general, hold Btn2 down for more than 2 seconds, wait for the menu display to return.
With the first test BtnReport() when you hold btn2 down long enough LED2 will go bright and “[ESC]” will be printed so you know it works. In this case, in order to exit you must then also press Btn1, while still holding btn2 down.