Mechanical Parts List
Ref	No	Size	Component	Notes
1	2	125 x 125 x 6mm	end support bottom plate	aluminium plates drilled and tapped as per drawings
2	2	125 x 125 x 4mm	end support top plate	aluminium plates drilled and tapped as per drawings
3	1	125 x 125 x 6mm	centre support bottom plate	aluminium plate drilled and tapped as per drawings
4	1	125 x 125 x 6mm	centre support top plate	aluminium plate drilled and tapped as per drawings
5	2	6mm	top load cell spacer	aluminium sized and drilled as per drawings
6	2	2mm	bottom load cell spacer	aluminium sized and drilled as per drawings
7	2	2kg	load cells and HX711 interface boards	style as pictured
8	2	44mm x 19mm x 33 inches	hardwood rail	sized and drilled as per drawings
9	4	SK16	bearing support	SK16 shaft end supports
10	1	M10	arrow stop	partial thread bolt with head removed
11	1	10mm	arrow stop support	rigid shaft coupling 10mm bore
12	1	8mm	arrow stop support	rigid shaft coupling 8mm bore tapped to M10
13	2	76 x 5mm	arrow support rod	5mm diameter carbon fibre rod
14	4	8 x 16 x 5mm	arrow support rod bearing	ball bearing races
15	4	5 x 8 x 5mm	bearing to rod spacer	spacers 5mm bore, 8mm OD length 5mm
16	4	16 x 5 x 1mm	bearing to locking collar washer	Teflon washers 5mm bore, 16mm OD, 1mm thick
17	4	5mm	shaft locking collar	5mm bore
18	4	5mm	arrow locating ‘O’ ring	5mm ID
19	8	M5	end bottom plate clamping ‘T’ nuts	Unbarbed
20	8	M5 x 24mm	end plate clamping bolt	CSK bolts
21	8	M5 x 30mm	centre plinth clamping bolt	CSK bolts
22	8	M4 x 8mm	arrow stop support bolt	cheese head screws
23	8	M4 x 12mm	SK16 bolt	cheese head screws
24	2	M4 x 22mm	load cell mounting bolt	CSK bolts
25	2	M5 x 22mm	load cell mounting bolt	CSK bolts
26	1	½ inch	arrow stop gauge	ball bearing to set arrow stop height
27	1	1kg	reference weight	for load cell calibration
28			shielded cable	shielded wire to connect HX711 boards to control box

ID – inside diameter
OD – outside diameter
CSK – countersunk