PROBABILITY is an important concept in physics. / Here, two dice are thrown and their sum is calculated. / The occurrences of each sum is displayed vertically. / The expected odds are shown by possible sums: / The display uses a 16x16 array of WS2812b LED, and an ESP8266 CPU (a Wemos D1 Mini). A single pushbutton switch is used to roll the dice. / The display shows the roll as pips for the two dice (green). / The total of the dice is shown as a number on the right (blue). / The display plots how many times each total was rolled (red). / Once any total reaches 16 times (the top), the run stops. / A second mode rolls the dice 1000 times for each press of the pushbutton. The sums are divided by 1000. This display looks closer to the expected distribution. / Push the button to advance and roll. / You can hold the button down to roll repeatedly.